## Slide 1: LED Design
Arduino Team
FRC226

## Slide 2
LED Module Design (Schematic)
GND
SDA
SCL
I2C
Power
GND
VIN

## Slide 3
LED Module Design (Wiring Diagram)
GND
SDA
SCL
I2C connector
Power (Battery)
GND
VIN(12V)
Capacitor
Resistor (220 Omh)
Metro Mini

## Slide 4
Programming on LED module
Install the NeoPixel and Arduino thread libraries
Load the NeoPixels_device.ino to the LED module
  Revise the constant as needed (#pixels, device id)
    #define NUMPIXELS 8
    #define I2C_DEVICE_ID 8
Use the Arduino UNO as the master for testing (code i2c_mater.ino attached)
Arduino
UNO
GND
SCL (A5)
SDA (A4)
LED#1
GND
SCL
SDA
master
slave
GND
5V

## Slide 5
Name | data length #bytes | command |  |  |  |  |  | 
 |  | byte 0 | byte 1 | byte 2 | byte 3 | byte 4 | byte 5 | byte 6
Color gradient mode | 5 | 0 | addr | count | mode | Step interval |  | 
Set color to a specific pixel | 5 | 1 | addr | red | green | blue |  | 
Activate the pixels | 1 | 2 |  |  |  |  |  | 
Enable serial line (rs232) debug console | 1 | 3 |  |  |  |  |  | 
Disable serial line (rs232) debug console | 1 | 4 |  |  |  |  |  | 
Reset, black out all pixels | 1 | 5 |  |  |  |  |  | 
Set color to all pixels | 4 | 6 | red | green | blue |  |  | 
Set color to a subset of pixels | 6 | 7 | addr | count | red | green | blue | 
Show blinking pattern for a subset of pixels | 7 | 8 | addr | count | red | green | blue | cycle interval
Show shifting pattern for a subset of pixels | 6 | 9 | count | red | green | blue | step interval | 
 | Parameter Name | Meaning |  |  |  |  |  | 
 | addr | pixel address (0, #NUMPIXEL) |  |  |  |  |  | 
 | count | number of pixels |  |  |  |  |  | 
 | mode | 0 - red, 1 - green, 2 - blue, 3 - RG, 4 - GB, 5 - RB, 6 - RGB, 7 - R<->B, 8 - G<->B, 9 - R<->B |  |  |  |  |  | 
 | red | (0-255) |  |  |  |  |  | 
 | green | (0-255) |  |  |  |  |  | 
 | blue | (0-255) |  |  |  |  |  | 
 | step interval | unit: milliseconds |  |  |  |  |  | 
 | cycle interval | Unit: 0.1 second |  |  |  |  |  | 
LED I2C interface programming
Write control code to LED module via master-to-slave write function
Control code
Read 1-byte (LED status) via master-to-slave read function
Status code
data length # bytes | byte 0
1 | status: 0 - idle, 1 - busy
Start
LED status busy?
End
Yes
No

## Slide 6
I2C connector
FRC Controller
GND
SCL
SDA
LED#1
LED#2
LED#N
GND
SCL
SDA
GND
SCL
SDA
GND
SCL
SDA
…
Integration on Robot
https://forums.ni.com/t5/FIRST-Robotics-Competition/roboRIO-Details-and-Specifications/ta-p/3494658
master
slave
GND
5V

## Slide 7
Tasks to be completed
Task | Leader | Date
Lab coordination (picking up the ordered parts, soldering station preparation, etc.) | Kristian | 2/14
Building LED modules | Aarti | 2/14
Flashing the software (NeoPixels_device.ino) to the LED modules | Sachin | 2/14
Installing LED modules to the FRC robot | Archana | 2/14
Programming on FRC robot (Java) | Christine Zeng & Shriya Shah | 2/14
Testing the LED system on FRC robot | Christine Zeng & Shriya Shah | 2/14